## Slide 1: ZONER
Harry Hoa Huynh
5/2021

## Slide 2: GOAL: To Develop an IoT Eco System
Features:
Connect multiple networks of sensors
Monitor sensor data
Notification/Alert/Feedback actions via actuators
Key Characteristics:
Easy to use
High data rate
Reliable
Low cost
Scalable

## Slide 3: Presentation Agenda
High Level Design
Hardware Design
Software Design
  Data Collecting and Processing Design
  Alert System Design
Demo
Feedback and Concern
Acknowledgement and Reference
Conclusion

## Slide 4: HIGH-LEVEL DESIGN

## Slide 5: HIGH-LEVEL ARCHITECTURE
Sensor#1
Sensor#2
Sensor#n
WIFI
Microcontroller
Local Control Hub
AWS
Design Option#1
Design Option#2
Sensor Network #2
There are 2 design options:
Data is pushed directly to Cloud, where it will be stored, processed, and monitored.
Data is uploaded, processed, and monitor at a local Control Hub.
For the scope of this project ‘ZoNer’: a system is used to monitor environmental parameters around a specific space such an office or small room.
Dashboard Monitor
Alert System
WIFI
WIFI
Sensor Network #1
WIFI
Microcontroller
Client Layer
Control Layer
Feedback Layer
Actuator System
Sensor Network #n
Notes: Split up to 3 different layers
Client layers: Multiple networks of sensors/ multiple transmitter such as WIFI MCU
Control layers
Feedback

## Slide 6: DESIGN OPTION#1: BLOCK DIAGRAM
MQTT
Dashboard Control
Via WIFI
Via Wireless
On Cloud
Actuator System
MQTT
Via WIFI
Alert System
Sensor Network #1
Sensor Network #2
Sensor Network #n

## Slide 7: TERMINATE DESIGN OPTION #1
Early experiment shows significant daily cost with an average of $5 to use simple min/max functions on single sensor data set.
Cost mainly is around these services:
AWS Key Management Service
Amazon Kinesis
Amazon Kinesis Analytics
After unsuccessful discussion with AWS and hours searching ways to activate Educate Starter Account or to earn AWS credit, there’s no choice but to move to Option#2 to maintain low service cost.

## Slide 8: DESIGN OPTION#2: INITIAL BLOCK DIAGRAM
MQTT
Dashboard Control
Via WIFI
Via Wireless
Actuator System
Via Localhost
Alert System
MQTT/Wired
MQTT
Sensor Network #1
Sensor Network #2
Sensor Network #n

## Slide 9
Design Option#2 is a good solution:
Open-source environment -> NO COST to LOW LOST
Scale up on your own will with also NO COST to LOW COST

## Slide 10: HARDWARE DESIGN

## Slide 11: AVAILABLE HARDWARE
ESP32-DevKitC-32D:
BLE/Wifi
Low cost
Rasp Berry Pi 3
UV Sensor
VEML6075
Pressure sensor
ST LPS22HB
Temperature
& Humidity
ST HTS221
Ambient Light
Sensor
TEMT6000
Environmental sensors Module
ESP32 Feather:
BLE/WIFI
Low cost
Temperature& Humidity
DHT11
10k Potentiometer
LEDs
iPhone
Desktop
Client Layer
Control Layer
Feedback Layer

## Slide 12: FINAL BLOCK DIAGRAM
I2C/Analog
MQTT
Via wires
Via WIFI
Via Wireless
Via Localhost
MQTT
1-Wire
Analog
MQTT
Via WIFI
IFTTT & Webhook
Client Layer
Control Layer
Via Wires
Via wires
Via wires
Feedback Layer
Network of sensor #2
Network of sensor #1
Zone#01
Zone#01
Notes: Explain on Potentiometer
IFTTT offers many services:
*Phone/Email/HTTP/MQTT, etc.

## Slide 13: WIRING DIAGRAM
USB Power
3.3V
J2:#1
#VCC
GND
J3#1
GND
SCL
J3:IO22
#12:SCL
SDA
J3:IO21
#11:SDA
Analog
J3:IO33
A2
J3:IO3
Wi-Fi Router shall be within 50 meters of the sensor network and PI
Debugging LED
Sensor Network can be located at any interested space within 50 meter of Wi-Fi router
Pi can be located at any interested space within 50 meter of Wi-Fi router
USB Power
Data
1-wire
IO33
GND
3.3V
Analog
USB Power
Zone#1 Alert/Actuator
For Network of Sensors#1
Zone#2 Alert/Actuator
For Network of Sensors #2
GPIO3
GPIO 3,11, 12
GPIO 13, 15
GND

## Slide 14: WIRING DIAGRAM
Network of sensor #1
Network of sensor #2
Control Hub with Alert Indicator/Actuator
LED#1 (Green): Blinking LED indicating PY working
LED#2: Zone01 Alert for Temperature
LED#3: Zone01 Alert for Lux
LED#4: Zone02 Alter for Temperature
LED#5: Zone02 Alert for Pot. Voltage

## Slide 15: SENSOR SPECS
Network of Sensors # 1 |  |  |  |  | Network Sensor #2 | 
 | LPS22HB | TEMT6000 | VEML6075 | ST HTS221 | DHT11 | Potentiometer functioned as a test sensor
Functionality | Atmospheric pressure | Ambient lux | UV A/B | Temperature and Humidity | Temperature and Humidity | Voltage
Input Voltage (V) | 3.3 | 3.3 | 3.3 | 3.3 | 3.3 | 3.3
Min Current on-time(uA) | 3 | 0.003 | 0.8 | 0.5 |  | 0
Typical Current on-time (uA) | 12 | 50 | 480 | 2 | 2.5 | 150
Max Current on-time(uA) | 12 | 750 | 480 | 2 |  | 330
Data output | 1. 24-bit pressure data 2. 16-bit temperature data | 1. 12-bit data lux from ESP32 ADC | 1. 16-bit UVA data 2. 16-bit UVB data | 1. 16-bit temperature data 2. 16-bit humidity data | 8-bit data | 1. 12-bit data voltage from ESP32 ADC
Min Power consumption (mW) | 0.0099 | 0.0000099 | 0.00264 | 0.00165 |  | 
Typical Power consumption (mW) | 0.0396 | 0.165 | 1.584 | 0.0066 | 0.00825 | 0.495
Max Power consumption (mW) | 0.0396 | 2.475 | 1.584 | 0.0066 |  | 
Communication Protocol | I2C | Analog | I2C | I2C | Single wire | Analog
Expected size of package per transmission (bit) | 40 | 12 | 32 | 32 | 8 | 12
Datasheet | LPS22HB | TEMT6000 | VEML6075 | HTS221 | DHT11 | 

## Slide 16: POWER BUDGET ON SENSOR NETWORK
Network of Sensor #1: ESP32 Power + All Sensors | 
Typical Power Consumption per transmission (mW) | 793.7952
Minimum Power during Hibernation (mW) | 0.5049
Package size per transmission (bit) | 116
Expected number of transmission per day | 2880
ESP32 | 
Wifi chip | ESP32­
Input Voltage (V) | 3.3
Min active transmitting Current (mA) | NA
Typical active transmitting Current (mA) | 240
Max active transmitting Current (mA) | NA
Modem sleep (mA) | 68
Light-sleep (mA) | 0.8
Deep sleep (uA) | 150
Hibernation (uA) | 5
Min Transmission Power (mW) | NA
Typical Transmission Power (mW) | 792
Max Transmission Power (mW) | NA
Deep Sleep Power (mW) | 0.495
Communication Protocol | Wifi
Datasheet | ESP32­WROOM­32D
Network of Sensor #2: ESP32 Power + All Sensors | 
Typical Power Consumption per transmission (mW) | 793.50325
Minimum Power during Hibernation (mW) | 0.99825
Package size per transmission (bit) | 28
Expected number of transmission per day | 2880
Notice that power of network sensor is high though it transmits less sensor data, majority of power consumption goes through the Potentiometer (which is a voltage divider between 3.3V and GND)

## Slide 17: SAVE POWER METHODS
Publish data every 30 seconds from ESP32
Disconnect WIFI and MQTT clients every 30 seconds, and only re-establish WIFI and MQTT connection before publishing data
EPS32 + Sensor Network stays in the Deep Sleep Mode, and only wake up every 30 seconds to capture and send data, then go back to the Deep Sleep mode
Future action: reduce size of package (size of raw data) to speed up the transmission and reduce power for future scale up

## Slide 18: SOFTWARE DESIGN

## Slide 19: DATA FLOW
Collect Sensor Data
Send Sensor Data to PI
Subscribe Data to all topics
Save Subscribed Data to Influx DB
Monitor Data using Grafana GUI
Display to Dashboard
Alert Notifications to Email
MQTT
ESP32
PI
Every 30s
Process Data in PI
Send alerts to Actuator/Indicator (LEDs)
Wires
Every 30s
Send alerts to Phone
IFTTT & Webhooks
Client Layer
Control Layer
Feedback Layer
Wire
Wireless
Notes: Key: Publish data every 30 seconds.

## Slide 20: DATA
Total raw data per transmission: 116 bits (network#1) and 28 bits (network#2)
Total number of transmission per day: 2880 times (once every 30 seconds))
Total number of raw data transmitted per day: 334,080 bits (network #1) and 80,640 bits (network#2)
Network of Sensor #1 |  |  |  |  |  | 
MQTT Package | #1 | #2 | #3 | #4 | #5 | #6
Type/topic | Pressure | Temperature | Humidity | Lux | UVA | UVB
Raw Data (bit) | 24-bit | 16-bit | 16-bit | 12-bit | 16-bit | 16-bit
Network of Sensor #2 |  |  | 
MQTT Package | #1 | #2 | #3
Type/topic | Temperature | Humidity | Voltage
Raw data (bit) | 8-bit | 8-bit | 12-bit

## Slide 21: Development Tools/Service
Visual Studio with PlatformIO:
  To program/debug ESP32 modules
  Develop in C
Python
  Develop in Python scripts for Pi data collection and data analytic
  Debugging in Py
IFTTT Service
  Wireless Notification
Webhook Service
  Wireless Notification
MQTT Service
  Data Collection
Grafana Service
  Dashboard and wireless notification
InfluxDB Service
  Data Collection

## Slide 22: MQTT VS HTTP
Why MQTT (Message Queuing Telemetry Transport):
Data centric (vs. document centric)
Light weight with short message header
Minimal message length : 2 bytes
Maximal message length: 265 bytes
93 time faster than HTTP (using 3G networks)

## Slide 23: ESP32 – PI COMMUNICATION: MQTT
Publisher
MQTT Broker
Mosquitto
Subscriber
Network#1 Publishing with location “Zone#01”:
“Humidity” via Humidity Topic
“Temperature” via Temperature Topic
“Pressure” via Pressure Topic
“UVA” via UVA Topic
“UVB” via UVB Topic
“UV Index” via UV Index Topic
“Lux” via Ambient Light Topic
Network#1 Publishing with location “Zone#02”:
“Pot Voltage” via Pot_Voltage Topic
“Temperature” via Temperature Topic
“Humidity via Humidity Topic
Notice that: 2 networks have the same topic name, but their locations are different.
Publish all the topics
Subscribe to all the topics
Influxdb Database
Every 30s
Notes: Explain the same topic, but different location

## Slide 24: MQTT@EP32/Zone01
MQTT@PI

## Slide 25: MQTT Debugging
The log shows debugging message generated by Python script on Raspberry Pi.
Integer number: debugging counter, increase by 1 every time mqtt_client.loop_start() is called.
Data from 2 networks of sensors (Zone01 and Zone02)
Alert via debugging window on pot_voltage of Zone 02

## Slide 26: InfluxDB@PI
Data is separated in 3 domains:
Type of measurement
Location
Data value
Notes: Json body

## Slide 27: Alert/Notification/Actuator

## Slide 28: IFTTT Alert from Pi
LED Alert
IFTTT Alert with Webhooks
Conditions

## Slide 29: IFTTT Alter on Phone
Alert/Notification: flow from Control Hub to IFTTT Server to Phone

## Slide 30: Alert on Dashboard
Alert bar
Alert text
Notes: Lux or any data can be used for Home Protection

## Slide 31: Alert on Control Hub
Zone 2: Voltage Alert
Zone 2: Temperature Alert
Zone 1: Lux Alert
Zone 1: Temperature Alert
Blinking Debugging Indicator to verify if the Python code is functional

## Slide 32: Email Notification from Grafana

## Slide 33: ZoNer DEMO

## Slide 34: Dashboard Monitor- Working Great

## Slide 35: Alert System: Working Great

## Slide 36: Conclusion
ZoNer is a solid foundation for future IoT applications. It offers many great features that make it a great building blocks for many IoT application in the field of data monitoring. 5 key characteristics: easy to use, high data rate, reliable, low cost, and easy to scale up are met in the ZoNer.
Future Improvement:
  Power budget
  Increasing the number of sensors for testing
  Optimizing the code
  Developing Printed Circuit Board
  Designing housing
  Optimizing the whole design.
It has been a great journey, and future ZoNer is hopeful to be on the market one day in the near future!